## Slide 1
Learning an Interpretable Traffic Signal Control Policy
James Ault | Josiah P. Hanna | Guni Sharon
arXiv: 1912.11023v2 | 2020
Presented by:
Assignment Presentation

## Slide 2
Presentation Outline
1. Motivation & Objective of the Paper
2. Key Techniques & Algorithmic Approaches
3. Experimental Setup
4. Main Results & Interpretation
5. Limitations & Future Scope
6. Conclusion & Key Takeaways

## Slide 3
Motivation & Problem Statement
The Interpretability Gap in Traffic Signal Control
• Traffic congestion costs billions annually in fuel, time, and emissions
• Reinforcement Learning with DNNs can reduce vehicle delay by up to 73%
• However, DNNs are black boxes — decisions cannot be explained
• Government agencies require interpretable, auditable controllers
• Current RL approaches are impractical for real-world deployment
Core Research Question Can we design traffic signal controllers that are BOTH high-performing AND human-interpretable? Performance (DNN) vs. Interpretability
Why Interpretability is Non-Negotiable • Liability: Who is responsible if an accident occurs? • Regulation: Agencies must approve control logic • Trust: Engineers need to understand & tune the system • Safety: Black-box failures can be catastrophic Traffic signals are safety-critical infrastructure.

## Slide 4
Paper Objective & Contributions
Objective: Design interpretable, regulatable control policies for traffic signals that match deep neural network performance while remaining fully human-understandable and tunable.
Six Key Contributions:
1. Formally define a "regulatable" control function for signal control
2. Compare regulatable functions against DNN-based policies
3. Study three optimization methods: CMA-ES, PPO, Deep Q-Learning
4. Develop three novel DQN variants using regulatable functions
→ DRQ, DRSQ, DRHQ (core technical contribution)
5. Evaluate on simulations of real intersections with observed traffic demand
6. Compare against deployed actuated controllers (practical baseline)

## Slide 5
Key Concept: Regulatable Control Function
Formal Definition A precedence function g(s, Φ; θ) is regulatable if for every state variable s[i]: ∂g/∂s[i] ≥ 0 for all states, OR ∂g/∂s[i] ≤ 0 for all states i.e., monotonic input-output relationships.
Practical Intuition "Green was given to Phase 4 BECAUSE stopped Southbound vehicles increased while Eastbound queue decreased." Every decision has a human-readable reason. Engineers can adjust individual weights.
State Variables (per traffic phase):
1. Stopped vehicles count
2. Approaching vehicles count
3. Cumulative stopped time
4. Average stopped time
5. Average queue length (stopped vehicles / lane count)
6. Average approaching vehicle speed
Polynomial Precedence Function:
g(s, Φ; θ') = Σφ∈Φ Σi=1..6 (wi · s[i])^pi × Σj=1..4 (w'j · fj)^p'j
• Weights (w) and exponents (p) per state variable per phase
• For 8-phase intersection: 256 total tunable parameters
• Proven regulatable via Lemma 1 (monotonic partial derivatives)

## Slide 6
Algorithmic Approach: Three Deep Regulatable Q-Learning Variants
Core Idea: Train a powerful DQN (black-box) first, then train the interpretable function G to imitate it.
DRQ Deep Regulatable Q-Learning Goal: G(s,a) = Q(s,a) (Match exact Q-values) Loss: Squared error (y - G(s,a;θ))² Problem: Polynomial cannot replicate full DNN capacity Result: Worst performer
DRSQ Deep Regulatable Softmax Q Goal: G(s,·) ∝ Q(s,·) (Match relative ranking) Loss: Cross-entropy between softmax(Q) and softmax(G) Insight: Proportional equivalence is sufficient Result: Good performer
DRHQ (Best) Deep Regulatable Hardmax Q Goal: argmax G = argmax Q (Match only the winning action) Loss: Cross-entropy between one-hot(argmax Q) & softmax(G) Insight: Maximum flexibility, only policy equivalence needed Result: Best performer
Progression: Match exact values (hard) → Match rankings (easier) → Match winner only (easiest & best)

## Slide 7
Alternative Optimization Methods: CMA-ES & PPO
CMA-ES (Covariance Matrix Adaptation Evolution Strategy)
• Type: Evolutionary / black-box optimization
• Few hyperparameters; handles continuous ranges
• Achieves near-DQN performance (validates function design)
Limitations:
• Needs 24 episodes per parameter update (very slow)
• Erratic exploration — unsafe during tuning
• ~4,000 episodes to stabilize (11 years of simulated traffic)
• Impractical for online / real-world deployment
PPO (Proximal Policy Optimization)
• Type: Policy gradient method
• Smooth, monotonic learning curves
• Bounded gradient steps ensure safe exploration
Limitations:
• Gets stuck in local optima (over-regularized)
• Suboptimal final convergence
• Cannot beat actuated control under high demand
• Insufficient for this domain despite safety benefits
Conclusion: Neither CMA-ES nor PPO are suitable for practical deployment. The DQN-based variants (especially DRHQ) are the most effective approach.

## Slide 8
Experimental Setup
Simulation Environment
• Simulator: SUMO (Simulation of Urban Mobility)
• Real traffic data from Utah DOT (2,092 intersections)
• Test site: State St & E 4500 S, Murray, Utah
• 10 traffic phases, 11 non-conflicting phase pairs
• >50,000 vehicles/day, peak rate: 95 cars/min
• 352 tunable parameters for regulatable policy
Traffic Demand Profiles
Low: 45,112 vehicles | 1.04 v/sec | Wed May 1, 2019
Medium: 51,298 vehicles | 1.19 v/sec | Mon May 6, 2019
High: 61,261 vehicles | 1.42 v/sec | Fri Jun 21, 2019
DQN Hyperparameters
• 3 hidden layers, 64 units each
• Replay buffer: 100,000 transitions
• Minibatch size: 32 | Optimizer: Adam
• Epsilon-greedy: 0.05 → 0 after 20 episodes
• Discount factor: 0.8 (low/med), 0.9 (high)
Baseline: Actuated Signal Controller
• SUMO’s actuated controller (used in real deployments)
• Phases in fixed order (protected lefts → through traffic)
• Maximum green time: 300 seconds
• This is what real intersections use today

## Slide 9
Main Results: Average Vehicle Delay Comparison
Average Vehicle Delay (seconds) — Lower is Better
Method Low Demand Medium Demand High Demand
Actuated (Baseline) ~60 sec ~70 sec ~95 sec
CMA-ES ~50 sec ~58 sec ~85 sec
PPO ~55 sec ~65 sec ~95 sec (fails in high)
DRQ Poor Poor Poor
DRSQ ~52 sec ~62 sec ~87 sec
DRHQ (Best Interpretable) ~50 sec ~60 sec ~85 sec
DQN (Black-box Upper Bound) ~48 sec ~57 sec ~82 sec
Key Finding: DRHQ achieves up to 19.4% reduced vehicle delay compared to deployed actuated controllers, while remaining fully interpretable. The gap vs. the black-box DQN is only 1–3 seconds.

## Slide 10
Interpretation of Results
Why DRHQ Works Best
• Only needs to match which action wins, not exact Q-values
• Gives maximum flexibility to the polynomial function
• Hardmax formulation directly targets policy equivalence
• Converges within a single episode for low/medium demand
• "Less is more": easier target = better practical fit
Why Other Methods Fall Short
• DRQ: Cannot approximate the full Q-function surface
• DRSQ: Softmax ranking harder to match than just the winner
• PPO: Over-regularized, converges to local optima
• CMA-ES: Requires thousands of episodes, unsafe exploration
• Pure polynomial/Fourier: Cannot complete basic scenarios
Critical Insight The performance gap between DRHQ (~50–85 sec) and the full black-box DQN (~48–82 sec) is only 1–3 seconds. This marginal cost buys complete interpretability — every decision can be explained, audited, and manually adjusted by traffic engineers. For safety-critical infrastructure, this is an excellent trade-off.

## Slide 11
Limitations & Future Scope
Limitations of This Work
• Single intersection only — transferability is unknown
• All results are from simulation (SUMO), no real-world test
• CMA-ES is impractical despite showing ceiling performance
• PPO fails under high demand scenarios
• No warm-starting from existing controllers explored
• 352 parameters still requires significant compute
• Limited to one geographic region (Utah traffic data only)
Future Research Directions
• Warm-starting from currently deployed controller behavior
• Multi-intersection coordination & network optimization
• Real-world deployment and field testing validation
• Transferability studies across intersection types
• Incorporating pedestrian and cyclist signal phases
• Adaptive parameter count based on intersection complexity
• Integration with connected & autonomous vehicle data

## Slide 12
Conclusion & Key Takeaways
1. Interpretable polynomial policies CAN match DNN performance (gap ≤ 1–3 sec)
2. DRHQ (Hardmax variant) achieves 19.4% delay reduction vs. actuated controllers
3. "Regulatable" = monotonic input-output relationship = human-understandable decisions
4. Policy gradient methods (PPO) are unsuitable for traffic signal optimization
5. The paper bridges the gap between AI performance and real-world deployability
6. Interpretability is not a luxury — it is a requirement for safety-critical systems
"We can build AI systems that are both powerful and explainable. We do not always have to choose one over the other."

## Slide 13
References
[1] Ault, J., Hanna, J. P., & Sharon, G. (2020). Learning an Interpretable Traffic Signal
Control Policy. arXiv preprint arXiv:1912.11023v2.
[2] Mnih, V. et al. (2015). Human-level control through deep reinforcement learning.
Nature, 518(7540), 529–533.
[3] Schulman, J. et al. (2017). Proximal Policy Optimization Algorithms.
arXiv preprint arXiv:1707.06347.
[4] Hansen, N. (2006). The CMA Evolution Strategy: A Comparing Review.
Towards a New Evolutionary Computation, pp. 75–102.
[5] Lopez, P.A. et al. (2018). Microscopic Traffic Simulation using SUMO.
IEEE ITSC 2018.

## Slide 14
Thank You
Paper: arXiv 1912.11023v2 | Authors: Ault, Hanna, Sharon (2020)
Presented by: